## Slide 1
HUMAN PERFORMANCE & PROLONGED FIELD CARE
Who needs a check, right now?
Wearables + operator dashboard + an agent that learns each person.
LIVE
REPLAY
SYNTHETIC
DefenseBio · SD Defense Hackathon · Oct 2026

## Slide 2
PROBLEM
Many people. One medic. No time.
WHO
needs a check?
WHAT
changed?
WHAT
was done?
DEFENSEBIO 02

## Slide 3
PRODUCT
One loop, sensor to reassessment
01
Capture
pulse · motion · button
02
Evidence
fresh? valid?
03
Compare
observed vs expected
04
Queue
reason attached
05
Act
check · ack · resolve
Alert = check the person or the sensor. Not a diagnosis.
DEFENSEBIO 03

## Slide 4
BUILT · HARDWARE
Two wearables. One mesh. 1 Hz.
WEARABLE ×2
Nano ESP32
LSM6DSOX + Polar HR
ROOT
ESP32 mesh root
USB serial
API
mesh_api.py
HTTP JSON
DASHBOARD
queue · map
check loop
57-byte packets · star topology · offline after 10 s · HR missing after 5 s
DEFENSEBIO 04

## Slide 5
BUILT · DASHBOARD
Alert → check → acknowledge → resolve
ATTENTION
Distress
button pressed
00:12
Physiology
HR +24 vs expected
00:41
Sensor
no samples 10 s
01:30
HR
112
bpm
EXPECTED
88
bpm
MOTION
0.4
g
Illustrative values. Screenshot goes here once the live demo runs.

## Slide 6
RESEARCH
Can an agent learn one person?
01
Build
02
Investigate
03
Transfer
04
Sustain
Test: agent vs direct personal fit, same data, same budget, untouched session.
DEFENSEBIO 06

## Slide 7
BUILT · REAL-DATA ENVIRONMENTS
Three tasks. Baselines executed.
PULSE
10.0
bpm MAE
ridge vs 16.2 median
23 people
HEAT
0.220
°C MAE
elapsed time wins wearables
24 people
LOAD
29.3
W MAE
Pandolf ≈ ridge 32.3
48 people
Private-test, best conventional baseline. Person-grouped splits.

## Slide 8
PULSE TASK · PRIVATE TEST
The bar an agent has to beat
Chart: 
| Median | Spectral | Motion spectral | Ridge
MAE | 16.2 | 18.4 | 17 | 10
DEFENSEBIO 08

## Slide 9
FINDINGS SO FAR
The benchmark already catches traps
5.40 vs 4.70
bpm
LLM agent lost to simple AR (3rd of 6)
23.6 → 44.4
W
Best on dev, worse on test: overfit
72.7%
90% intervals covered only 72.7%
Small pilots. They prove the harness measures; not who wins.

## Slide 10
POST-TRAINING · CODE BUILT, NOT RUN
Environment → GRPO loop
RUNPOD
verl + vLLM
GRPO trainer
BEAM
network-blocked
agent sandboxes
SCORER
private labels
holdout reward
No GPU run yet. No checkpoint. No measured gain.
DEFENSEBIO 10

## Slide 11
STATUS TONIGHT
Done, partial, tomorrow
Mesh + dashboard
DONE
Pulse / Heat / Load envs
DONE
Live consented pilot
TOMORROW
Personal predictor
TOMORROW
Agent vs direct fit
PARTIAL
LLM judge
PARTIAL
GRPO training
PARTIAL
Trained checkpoint
NOT STARTED
DEFENSEBIO 11

## Slide 12
FINISHING TOMORROW
Prove the loop, live.
01
Confirm hardware
02
Pilot capture
03
Live demo loop
04
Agent vs direct fit
Not a diagnosis. Not clinical. Synthetic stays labeled.